Safety Review- Ag. Eng. 2

Basic power tool safety- disconnect from power source during service, avoid wet surfaces, use

of improper tool, Clean shop, first aid kits, sharp tools in pockets, Horseplay, Grounding, Reporting injuries

Eye Protection- safety glasses- ANSI Z8.1 standards

Safety colors- 	Red- indicates fire equipment

Orange- Warning and marks moving parts

Yellow- Caution- operating wheels, levers, other controls

Green or gray- used on body of power tools and benches

Green- first aid

Blue- “out of order” defective equipment tagged

Ivory- immovable edges of equipment, tops of benches, inside cabinets

Yellow and Black- marks raised entrances-door sills, center post

Welding Safety-	Arc-  Helmet w/ filter shade lens of #10, gloves, long sleeves, burns to eyes medicated with Butyn solution, ventilation

Gas-  Goggles, tip size, turn off acetylene first to prevent flashback, never use acetylene pressure over 15psi, use of spark lighter

Drilling- size-, lubricant- reduce friction, lub drill, absorbs heat

-hold in a drill press vise, center punch, reduce pressure before breaking through

Shop Space- open space for safe operation of stationary power equipment

Grinding and Filing- 1/8 inch max. between wheel and tool rest, using files w/o handles

- Grinding wheel dresser, File card- cleans file

Cold Chisel- Cape chisel- used for cutting narrow, flat grooves and keyways

Bolts- Machine vs. Carriage, bolt cutters designed to cut wrought iron and low carbon steel

Jack stands-

Hacksaw- apply pressure on forward stroke, min 3 teeth in contact with metal

Lighting- 300 watts for each 100 ft2

Door and window area- 25% of the floor space, equipment entrances 12-16 feet wide

# Service Area